WBS 1.6 FDR
 Full Spectrograph AIT
DESI Spectrograph:
in-situ Calibration System
Julien Guy (IN2P3/LPNHE)
Sonia Karkar (IN2P3/LPNHE)
Laurent Le Guillou (UPMC/LPNHE)
DESI France Workshop
Paris/Saclay, Nov. 17th-18th, 2016

---
Overview
Talk outline
Overview
Calibration System Requirements
Calibration light sources
Spectral lamps
Continuum lamps
Lambertian diffusion screen
Current status and planning

---
Telescope and Dome dimensions

---
Rationale
Spectral lamps to get the wavelength solution (CCD pixels to wavelength)
→ required : enough well separated atomic lines
Continuum lamps for flats (fiber to fiber uniformity)
→ required : a « flat » enough spectrum on the whole spectro range (350 – 1000 nm)
Spatial uniformity / pupil uniformity :
→ 4 identical boxes on the upper ring
→ A quasi perfectly lambertian diffusion screen

---
Calibration System Requirements (DESI-1067)
Req’t Name	Requirement	Rationale	Verification method
Bandpass	360-980 nm	Required for z range of Ly-alpha QSOs and ELGs / (DESI-0318)	Laboratory tests: measure lines lamps spectrum
Pupil Uniformity	20% (azimuthally averaged)	PSF stability of 3% req. IN.FBR-5013, / (DESI-0581 v8)	Measured lamp luminance plus analysis
Field Uniformity	5% (relative to the telescope field response to a constant sky intensity)	ELG redshift efficiency and catastrophic failure rate unchanged	Measured lamp luminance plus analysis
Spectral Line Coverage	Wavelength calibration precision better than 0.15 pixel or 0.08 A / (this requires “approximately” / a max. bright line separation of 40 nm)	Required for accurate spectral extraction. / (DESI-318)	Laboratory tests: measure lines lamps spectrum
Continuum flatness	Maximal spectral variation of a factor 10 (max/min) in counts	Calibration images above noise and below non-linear regime & brighter-fatter effect	Laboratory tests: measure continuum lamps spectrum

---
DESI Blue, Red and NIR arms bandpass

---
Pupil illumination uniformity (max 20%)
Pupil uniformity change of 20%
→ max change of spectro PSF FWHM < 0.2% ∀λ
Meets requirement on PSF stability of 3% (requirement IN.FBR-5013, see DESI-0581 (v8)).
Max diff <0.2%
Input 20%
non-uniformity
benchmark input
azimuthally average pupil intensity
pupil intensity at the fiber output
(with a measured the fiber FDR)

---
Field illumination uniformity (max 5%)
Field inhomogeneities → error on the fiber flat-fielding (calib. with continuum lamps)
→ sky background residuals in the target spectra
→ Science criteria : ELG redshift efficiency and catastrophic failure rate
5% flat field error
5% flat field error
The simulated ELG sample of the first redshift data challenge were fit with the zztop redshift fitter,with a fiber flat field error emulated by adding a fraction of the sky spectrum in the ELG spectra

---
Four Source boxes

---
Four Sources Boxes should be enough
First study by P. Jelinsky, using ray tracing 
Define need for 4 sets of lamps
Careful analysis of fiber to fiber uniformity
New code (J. Guy), purely geometrical, interfaced with DESI model
Reproduce previous results
Investigate effect of intensity variation of lamps On going
4 lamps
1 lamp
Screen illumination
View from fibers
1.6 deg off center
At focal plane center

---
Spectral sources (arcs): spectral lines coverage
Impact the wavelength solution:
Rough estimate with MC gives 40 nm max. spacing
Example with third pipeline data challenge (DC3) of DESI and SDSS/BOSS lines
→ combination of 3 - 5 lamps to get enough well separated lines:
Hg, Cd, Ar, Ne, Kr, Xe, Zn...
Lack of lines coverage affects the precision of the wavelength solution

---
Spectral sources candidates
Spectrum data from manufacturers / NIST atomic lines
Lines positions for combination of lamps HgCd, NeAr and Xe
Lines positions for pencil-lamps from Newport HgAr, Xe and Ne

---
Spectral sources candidates
Spectral sources candidates
Spectral sources candidates
Spectral sources candidates
Several manufacturers (UVP, Oriel, Philips, Osram, …)
But :
– Huge differences between lamps of containing the same atomic elements
– Unreliable lines relative intensities
– No photometric information
(except for some dangerous UV lines)
On-going tests (and analysis) for several models (UVP, Philips, Osram…) : spectra and photometric measurements (at LPNHE)

---
Example: Neon lamp (UVP PenRay)
Relative line intensity strongly differ from manufacturer data

---
Continuum lamps: spectral flatness
Requested : clean calibration signal above noise
     → Min number of electron per pixel row : 10 000 e⁻
Avoid high intensity non-linear effects
     → Max number of electron per pixel row : 168 000 e⁻
Ratio of DESI throughput across full spectral range = 5
     → Max ratio of counts across the spectrograph complete spectral range = 3
        very constraining
→ Becomes factor of 10 if use several exposures
        with different exposure time for each band

---
Continuum lamps
current continuum lamps (halogen) available at the Mayall
“low flux” lamps have a blue filter to balance their spectrum.
Coverage problems and flux instability with the existing continuum lamps
Discussion on a additional set of powerful LED (with P. Martini)
“low flux” lamp x15
“high flux” lamp

---
The existing screen is too small

---
Lambertian Screen upgrade
« Permaflect » coating :
→ Lambertian reflectivity
Replacing all panels for better uniformity
Flat and >90 %
on DESI range

---
OGSE Conclusions
Planning: milestones
- Final selection of lamps based on lab tests (end 2016)
- Order screen parts (mid-2017), mounting screen (end 2017)
- Final design of the sources boxes (early 2017)
- Sources boxes production and tests (end 2017)
- Mounting the boxes on upper ring (mid-2018)
- Tests and Commissioning (end 2018)